## Slide 1: Audio-visual noise removal in speech using a binary mask: exploiting correlations between lip contours and modulation envelopes
Arun Palghat Udayashankar

## Slide 2: Acknowledgements
Peter Jacobs - Mentor
Tracy Petrie - Discussions
John Condon - Behavioral Testing
Nick Preiser - Office mate
Navid Resalat - Office mate + discussions
Gabrielle Saunders (NCRAR) - Project conception
Meghan Stansell - Marking words in sentences
Funding: Career Development Award (CDA-1) C7693M to Peter Jacobs from the Dept. of Veterans Affairs

## Slide 3: Statement of the Problem
28 Million People in U.S. Suffer From Hearing Impairment
1 in 5 over age 70 are both legally blind and have hearing deficits (dual-sensory impaired)
Current Hearing Aid Technology is Unsatisfactory
  Amplification & Filtering is Primary Solution
  Directional microphones & binaural devices also used
  Speech in noise still a major problem
No solutions for dual-sensory impaired patients

## Slide 4: No shortage of noise removal options
Current methods for noise removal in hearing aids
  Directional microphones
  Adaptive microphone arrays
  Adaptive filtering
  Envelope modulation filters
    Atlas et al, 2005, Souza et al. 2005
  Spectral subtraction

## Slide 5: Modulation filtering
Steven Schimmel, University of Washington

## Slide 6: Modulators are important for speech intelligibility!
http://isdl.ee.washington.edu/projects/modulationtoolbox
Sixteen modulated harmonics
Sixteen modulators with fixed carriers
Sixteen carriers only
Notes: Present the clean signal first, show a cartoon of each condition (i.e. modulator + carrier, modulator alone, carrier alone)

## Slide 7: Noise Removal Methods Envelope modulation
Envelope modulation filtering
  Atlas et al. 2005
BP Filt 1
Env Detect
Smooth envelope
Carrier detect
BP Filt 1
In
Out
BP Filt 2
…
BP Filt N
X
S

## Slide 8: Evidence supporting use of visual information
People comprehend 50 - 60% more when presented visual + auditory information compared with auditory alone
Visual cues not used in hearing aid noise removal algorithms

## Slide 9: Lip height vs. modulation envelope
1
2
3
4
5
6
7
8
9

## Slide 10: Research Questions
Do lip contours correlate with modulation envelopes
  Simple sounds
  Words
  Sentences
If so, can we substitute modulation envelopes with lip contours to improve speech quality in noisy environments
Can visual cues such as lip contours improve classical acoustic noise removal signal processing algorithms
  Voice activity detection (VAD)
  Multi-band VAD
Notes: Animate each question so that viewer can be introduced to them one at a time.

## Slide 11: Prior work on audio visual noise removal
Consonant vowel recognition scores improve in an automated classifier and perceptual tests by including visual features
  Girin, Schwartz and Gang (2001)
Target speech source separation can be improved by using video features
  Sodoyer, Girin et al. 2004
Single band voice activity detection using Audio+ Video better than Audio alone
  Sodoyer et al. 2009
Nobody has integrated video features in a multiband VAD speech processing algorithm.

## Slide 12: Proposed futuristic system
Video camera wirelessly sends data
  Mounted on lapel…
  eye-glasses (Google glass)
Hearing aid receives the video features wirelessly

## Slide 13: Recording the audio visual corpus
Revised speech-in-noise (RSPIN) data corpus
Two speakers recorded (audio and visual) of face in anechoic chamber
Video recorded using 96 fps Basler black-and-white camera
Audio recorded using LYNX2B sound card, 24-bit resolution
Introduce white noise at different signal-to-noise ratios during post-processing

## Slide 14: Facial Feature Extraction
Visual feature (bv) extraction – 66 visual features around mouth, eyes, chin, nose and cheeks
Visual features include
  Height of outer lips
  Height of inner lips
  Width of mouth
  Height of upper-lip to chin
  Ellipse parameters fit to the outer lips
  Change in features over time

## Slide 15: Audio feature extraction
Speech at desired SNR
Sub-band filtering, envelope extraction
Correlation with lip height
.. 25 bands
Notes: Subbands illustration

## Slide 16: Simple sounds: R= 0.64 +/- 0.12 (N=90)
R value
Modulation envelope
Lip height
Udayashankar et al. ARO 2014
Notes: Graphic showing mod env for simple sounds

## Slide 17: Sentences: R = 0.38 +/- 0.07 (N=400)
R^2 value
Modulation envelope
Lip height
Notes: ARO reference; reverse histogram with the envelope and lip height

## Slide 18: Words: R = 0.45 +/- 0.08 (N = 727)
R value
Modulation envelope
Lip height
Notes: Add graphic showing mod envelope of a word

## Slide 19: Correlations between lip height and modulation envelope
Normalized magnitude of Lip height
Normalized magnitude of modulation envelope
Notes: Take out the information about swapping mod env with lips. Talk about that under research question 2.

## Slide 20: Summary : Lip contours vs. modulation envelopes
Do lip contours correlate with modulation envelopes?
  Yes, sentences, words and simple sounds’ modulation envelopes showed good correlations with lip height, increasing in that order.
Notes: Summary

## Slide 21: Research question 2: substitution of lip contours with modulation envelopes
Extract lip contour
Extract audio modulation envelopes for 16 bands
Maintain carrier for all bands
Replace modulation envelopes for lip contours
  All envelopes replaced
  Just lowest frequency envelopes
Notes: Summary

## Slide 22: Summary for research question 2
Despite the good correlation between lip height and modulation envelopes, swapping out the latter for the former does not lead to intelligible speech
Notes: Summary

## Slide 23: Research question 3: Improvement of Voice Activity Detection (VAD)
Can visual cues such as lip contours improve classical acoustic noise removal signal processing algorithms
  Multiband voice activity detection (VAD)
    Kim and Loizou, J Acoust Soc Am. 2009 Sep; 126(3)
      An algorithm that improves speech intelligibility in noise for normal-hearing listeners.
Notes: Summary

## Slide 24: Voice Activity Detection
Front end to hearing aid noise removal
Several other applications of VAD in addition to hearing aid algorithms
  VOIP telephony
  Speaker recognition algorithms
We are doing multi-band VAD
  Using Audio features
  Using Video features
  Using Audio and Video features
Notes: Summary

## Slide 25: Multiband VAD using a spectro-temporal binary mask
Samples
Time (s)
Frame
Frequency
Frequency band
Amplitude
Notes: Add the raw speech signal, then the spectrogram of the speech signal, then show the binary mask

## Slide 26
400

## Slide 27: Sub-band filtering
Map of pitch perception vs. frequency in Hertz
As frequency in Hz increases, it takes a larger increase in Hz to perceive a higher pitch
Due to the non-linear representation of frequencies in the cochlea
3 .
.
20 .
Notes: Add title to this slide, making it consistent with Audio Feature Extraction slide.

## Slide 28: Envelope extraction and windowing
Notes: Put in a figure for envelope extraction

## Slide 29: Features as sums under triangular filters
....................
FFT magnitude of each frame
*
1 2 3 ………………………………………… 14 15

## Slide 30: Video Features
Lip height (LH): mean(2-8,3-7,4-6)
Lip Width (LW): 1-5
Std(LH) across 5 frames
Std(LW) across 5 frames
1
2
3
4
5
6
7
8
9

## Slide 31: Classification: Overview
Oracle generation
Speech at 5 dB SNR (400 sentences)
Subband filtering
Ideal binary mask (Oracle for the classifier)
AV-Speech at desired SNR (400 training sentences)
Subband filtering, windowing and feature extraction
Train binary classifier
AV-Speech at desired SNR (400 test sentences)
Subband filtering, windowing and feature extraction
Apply model to predict binary mask
Remove noise using binary mask
Reassemble bands into clean speech
Evaluate using statistical and listening tests.
Training phase
Evaluation phase
Notes: Have this animate in from left to right

## Slide 32: Oracle generation
Speech
Noise
Subband filtering, envelope and framing of speech
Compute SNR for each frame
Subband filtering, envelope and framing of noise
Is SNR > threshold
Signal
Noise
N
Y
Notes: flow chart

## Slide 33: Oracle: example
SNR (dB)
MASK (binary)

## Slide 34: Training phase
Extract auditory features from “noised” speech files
Extract Oracle from clean speech
Train binary classifier
Produce statistical model
Notes: Train a linear classifier (linear regression) and a nonlinear model (GMM)

## Slide 35: Training phase: Linear regression model
Features fit to a model with a binomial distribution using logistic regression
  is voice activity detection (speech vs. noise)
  x are the audio (A), video (V) or audio + visual (AV) features
  is the vector of model parameters that will be fit
Prune those features that gave a bad fit (p < 0.05) one at a time
Pick a threshold to define as signal or noise
  Youden’s index was used to compute the threshold

## Slide 36: Training phase: Gaussian mixture model: model definition
D- dimension of feature vector
  45 For Audio
  4 For Video
  49 For Audio + Video
  C -
p – probability density function
  These get fit during GMM training
  {μ – mean D*N, Σ – covariance D*D*N; α – mixture weight 1*N}
Nmax = 2D
  N = number of mixture weights
  Nmax = max no. of mixture weights
Example: D=2, N=3
Notes: Check all definitions!

## Slide 37: Training: Greedy expectation maximization
Different from regular EM, you start with just 1 component.
Add in additional components by searching for optimal parameters one component at a time.
Optimize the parameters; add one more ..
Not dependent on initialization unlike simple EM.
Neural Computation, 5(2):469–485, Feb 2003.

## Slide 38: Training: Bayesian Classifier
Two Gaussian Mixture Models to model the distribution of feature vectors in each class (noise and signal)
Bayesian classifier to compute probability of the signal belonging to each class
  Priors = number of feature vectors belonging to the class/ total no of feature vectors (FV)
  (PriorSignal*p(FV|signal)) vs (Priornoise*p(FV|noise))

## Slide 39: Testing phase
Extract auditory features from “noised” speech files to be tested
Extract Oracle from clean speech
Use statistical model to predict binary MASK
(linear or non-linear)
Compute confusion matrix (percent correct for a given class)
Clean up speech files using predicted MASK
Listening test
Notes: Train a linear classifier (linear regression) and a nonlinear model (GMM)

## Slide 40: Performance assessment
Compare VAD accuracy
  A, V, and A+V
Receiver operator characteristic analysis
Confusion matrix of classifier
Intelligibility test
  TBD

## Slide 41: Multiband VAD: Area under the curve for linear model (0 dB, white noise)
Notes: Keep colors the same

## Slide 42: GMMBayes: classification accuracy
0 dB -8 dB

## Slide 43: -8 dB, white noise
Notes: Change the ordering, highlight visual processing alone..

## Slide 44: Summary of results
This is the first attempt to create a multiband voice activity detector using audio and visual features
  Multiband voice activity detector confirms results of single band voice activity detector using a linear model.
For the same features and SNR, the non-linear model targets noise much more effectively than the linear model
  In previous studies, the GMM-Bayes model has been show to be effective with audio features alone in removing noise at -5 dB SPL and specific to the noise type.
Combining video features with audio features provided an improvement in classification of signal than using audio features alone in the non-linear model.
Video features alone in the non-linear model are able to remove noise as effectively as using audio features alone at negative SNR.

## Slide 45: Thank you 
Github.com/puarun/AVproject

## Slide 46: Future directions
Listening tests of models with and without video features
Train and test models on:
  Other noise types: cafeteria, babble
  Same model with multiple noise types
  Multiple speakers

## Slide 47: END
Thank you for the opportunity to present my work to the department. 
Please sign up if you would like to volunteer for our listening tests.
Open for comments/ discussion

## Slide 48: Results: single band VAD
As SNR drops, the value of incorporating visual features can be observed
SNR = -6 dB, Cafeteria noise
Jacobs et al. IHCON 2012
A+V
V
A

## Slide 49: Linear regression: classification accuracy
0 dB SPL -8 dB SPL

## Slide 50: Mixture model example
Colors : mixtures (3)
Two features
  Mu (2*3)
  Sigma (2*2*3)
Gaussian mixture model
Feat 1
Feat 2

## Slide 51: Example : GLM at -8dB, white noise

## Slide 52: Delay between audio and video

## Slide 53: Previous work: GMM Bayes
Model specific to SNR (0 , -5 dB) and noise type (babble, speech shaped, factory)
  Very efficient at removing noise
  Results from behavioral test of models trained on a specific noise type come close to the IDBM
Shown to be very efficient at -5 dB SNR without video features
JASA Vol. 126 (3), Sep. 2003

## Slide 55: Linear 0 dB SPL

## Slide 56: GMMB 0dB SPL

## Slide 57: Testing: Audio reconstruction
J. Acoust. Soc. Am. 126 (3) , September 2009

## Slide 58: Confusion matrix
90 | 10
20 | 80
Actual
1 0
Predicted
0 1

## Slide 59: Linear model results: 0 dB -8 dB